## Slide 1: University of Padua – Department of Information Engineering Bachelor’s Degree in Control System Engineering
Embedded Real-Time Control Laboratory Activities and Key Concepts
Group 4:
Brescia Davide (2182457)
Favaro Manuel (2199436)
Filannino Daniele (2179425)
Padua, 19/02/2026

## Slide 2: LABORATORY 1
Configure and handle external interrupts;
Periodic line sensor reading using both polling
HAL_GetTick()
Hardware Timer Interrupt
Data acquisition from keypad and line sensor via I2C

## Slide 3: LINE SENSOR
Infrared line sensor Pololu QTR-MD-08RC
Integrated infrared LEDs and phototransistors
Communicates via I2C bus

## Slide 4: Periodic Polling Approaches
Busy-Waiting Polling
Non-blocking Polling
HAL_GetTick() as a software timer
Improved efficiency
CPU not blocked
Based on time comparison
Timer-Based Polling
Hardware timer every 100ms
Precise and reliable timing
CPU not blocked
Interrupt Service Routine ISR
Continuous polling
Simple but inefficient
CPU fully occupied

## Slide 5: KEYPAD SETUP
Numeric key (’0’–’9’)
Clear key (’*’)
Confirmation key (’#’)
Other keys (e.g., A, B, C, D)

## Slide 6
  BLINK() FUNCTION
Blocking Approach
Uses HAL_Delay()
Divison by zero check (freq = 0)
CPU blocked inside delay loop
Non-blocking Approach
Uses hardware timer with periodic callback
Software based counter
LED can blink without blocking CPU

## Slide 7: LABORATORY 2
Open-loop motor actuation using PWM signals
Data acquisition for motor model identification
Angular speed measurement using incremental encoders

## Slide 8: MOTORS
Forward
Reverse
Brake
Coast
Forward and Coast: the PWM alternates between forward drive and coast mode
Forward and Brake: the PWM alternates between forward drive and active braking

## Slide 9: ENCODERS
Data analysis performed in MATLAB:
Motors angular velocities (in rad/s)
Reference voltage (step input)

## Slide 10: Second Part – Motor Control
Identifying working points
Motor Parameters Estimation
PI Controller Design
Validation of Controllers
Windup Problem

## Slide 11: Working Points Identification
First ISSUE
Real-World non linearities
Behaviour of Left Motor
Behaviour of Right Motor

## Slide 12: Motor Parameters Estimation – Graphical Method
First Rough Estimate
(Baseline)
Fix
Find w.r.t. the 2% of
Find w.r.t. the 63.2% of
Compute as known
Repeat with different

## Slide 13: Motor Parameters Estimation – Tangent Method
Deterministic and more precise
Fix
Find inflection point and plot the tangent
Find as the intersection between the axis
Compute as known
Repeat with different

## Slide 14: Final Comparison
Motor 1 |  |  |  | 
Method | Input Step [V] |  |  | 
Graphical | 5.0000 | 2.6680 | 0.4700 | 0.0500
Tangent | 5.0000 | 2.3911 | 0.5842 | 0.0562
Motor 1 |  |  |  | 
Method | Input Step [V] |  |  | 
Graphical | 5.0000 | 2.6680 | 0.4700 | 0.0500
Tangent | 5.0000 | 2.3911 | 0.5842 | 0.0562
Motor 2 |  |  |  | 
Method | Input Step [V] |  |  | 
Graphical | 3.0000 | 3.9845 | 0.5800 | 0.0600
Tangent | 3.0000 | 3.9364 | 0.7382 | 0.0772
Motor 2 |  |  |  | 
Method | Input Step [V] |  |  | 
Graphical | 3.0000 | 3.9845 | 0.5800 | 0.0600
Tangent | 3.0000 | 3.9364 | 0.7382 | 0.0772

## Slide 15: PI Controller Design
Ziegler-Nichols method based on open-loop response
First Rough
Approach
Results in a too aggressive response
Second Refined Approach
Manual Tuning based on Matlab Simulations
PI gains adequately modified to achieve a tradeoff between smoother/faster dynamics
?
?
Results in a too aggressive response

## Slide 16: PI Controller Design - Results
PI tuned following Matlab ideal response
Speed Reference of

## Slide 17: Combined Cross Validation
Individually each motor performs well…
But they need to work together!
So, what about their combined responses?
We performed several tests with dynamic reference speeds
Slightly modified PI gains to achieve close dynamics
Satisfactory results, but we were not done yet

## Slide 18: Windup Problem
A problem arose when we ran the code the first time
Similar problem if motors were not powered on!
Input computed by the STM32 with
unreachable reference of
This results in…

## Slide 19: Anti-Windup Design
The solution is to implement an Anti-Windup
Clamps the integral error to match physical motor limits
Useful either when the motors are not powered on or when the reference is unreachable
Input computed by the STM32 with
unreachable reference of

## Slide 20: LABORATORY 4
Objective
Follow the line and achieve the fastest lap time.
Circuit A: Bullet
Circuit B: Hourglass
Notes: Objective: follow the line and get the fastest lap speed! We have created the bilding blocks.
, two different tracks, first approach, just see if it was on the left turn left, if it was on the right turn right.

## Slide 21: Controller Architecture
Calculating
Kinematic Conversion
Computed as a weighted mean of the photodiode readings.

## Slide 22: Tuning Parameters
Driving mode (FC o FB)
We have choosen FC
Reference Speed (V):
Set slightly lower than the max speed reachable by Motor 1
Proportional gain (K):
Initially set as low as possible to complete the track
Resulted in High K value, which led to vibrations
Solution was to increase K when was high

## Slide 23: Circuit A: Bullet
Lap Time [s] | Avg. Angular Speed [rad/s] | Avg. Linear Velocity [m/s] | Estimated Distance [m]
19.38 | 5.87 | 0.20 | 3.87

## Slide 24: Circuit B: Hourglass
Lap Time [s] | Avg. Angular Speed [rad/s] | Avg. Linear Velocity [m/s] | Estimated Distance [m]
22.07 | 6.49 | 0.22 | 4.87

## Slide 25: LABORATORY 5
Redesign of sequential algorithm into independent tasks:
  Line Task: handles line detection
  Control Task: executes vehicle control logic
  Communication Task: manages data exchange
Periodic execution is handled through osDelayUntil(10) → ensures no jitter
Objective
Conversion to FreeRTOS

## Slide 26: Task Managment
Prevent
concurrent access with a Mutex
controlTask
communicationTask
Telemetry data
Sensor data
Get
Put
Release
Acquire
Queue
lineTask
(global variable)
Ensure synchronization with a Sempahore

## Slide 27: Noisy Track
Problem: TurtleBot successfully followed the line on all section, but fails on the gray line.
Proposed solution: Implement a behaviour based on prior knowledge of the circuit layout.

## Slide 28: Following an Invisible Line
Line
Detected
Line
Lost
Turn
Right
Control Parameters:
Rotation trigger condition
Rotation Magnitude
■ Ideal
■ Late or Under Rotation
■ Early or Over Rotation

## Slide 29: Final Result